Testspecification for the TeaTimer Application

# Parameter configuration
### Read parameters via serial interface

Requirement:	Verify that parameters can be read via the serial interface.

Test setup:	Configure the device for simulated temperature input via serial	connection.
Send temperature data that puts the device out of pre-heat mode.
Check that the device is in measurement mode.

Test steps:	1. Send the string “Get Param $Param” via serial connection.
2. Wait for the answer of the device.
3. Check that the answer is of the expected data type $dType.

Test parameters:
This test needs to be done for all readable parameters.
Parameter name	$Param	$dType
Refresh rate	refreshRate	int
Target temperature	targetTemp	double
Cold temperature	coldTemp	double
WLAN SSID	SSID	string

### Write parameters via serial interface with valid values

Requirement:	Verify that parameters can be written via the serial interface when the	written value is of the correct data type and in the allowed range.

Test setup:	Configure the device for simulated temperature input via serial	connection.
Send temperature data that puts the device out of pre-heat mode.
Check that the device is in measurement mode.

Test steps:	1. Send the string “Set Param $Param $Value” via serial connection.
2. Wait for the answer of the device.
3. Check that the answer of the device is “OK”.
4. Send the string “Get Param $Param” via serial connection.
5. Wait for the answer of the device.
6. Check that the answer is $Value.
Test parameters:
This test needs to be done for all writable parameters.
Parameter name	$Param	$Value
Refresh rate	refreshRate	5 [seconds]
Target temperature	targetTemp	77.5 [degree Celsius]
Cold temperature	coldTemp	-1.0 [degree Celsius]
WLAN SSID	SSID	My Home Network

### Write parameters via serial interface with invalid values

Requirement:	Verify that writing a parameter with an invalid value does not change	the parameter. The device should not crash.

Test setup:	Configure the device for simulated temperature input via serial	connection.	Send temperature data that puts the device out of pre-heat mode.	Check that the device is in measurement mode.

Test steps:	1. Send the string “Set Param $Param $Value” via serial connection.	2. Wait for the answer of the device.	3. Check that the answer of the device is “ERROR”.	4. Send the string “Get Param $Param” via serial connection.	5. Wait for the answer of the device.	6. Check that the answer is not $Value.

### Write parameters and check reaction of the output

Requirement:	Verify that written parameters are reloaded in the system by observing	a change in the output.
Test setup:	Configure the device for simulated temperature input via serial	connection.	Send temperature data that puts the device out of pre-heat mode.	Check that the device is in measurement mode.

Test steps:

# Data processing

# Performance tests