Testspecification for the TeaTimer Application

# Parameter configuration
### Read parameters via serial interface

Requirement:	Verify that parameters can be read via the serial interface.

Test setup:	Configure the device for simulated temperature input via serial	connection.
Send temperature data that puts the device out of pre-heat mode.
Check that the device is in measurement mode.

Test steps:	1. Send the string “Get Param $Param” via serial connection.
2. Wait for the answer of the device with a timeout of 200 ms.
3. Check that the answer is of the expected data type $dType.

Test parameters:
This test needs to be done for all readable parameters.
Parameter name	$Param	$dType
Refresh rate	refreshRate	Int
Target temperature	targetTemp	Double
Cold temperature	coldTemp	Double
WLAN SSID	SSID	String

### Write parameters via serial interface with valid values

Requirement:	Verify that parameters can be written via the serial interface when the	written value is of the correct data type and in the allowed range.

Test setup:	Configure the device for simulated temperature input via serial	connection.
Send temperature data that puts the device out of pre-heat mode.
Check that the device is in measurement mode.

Test steps:	1. Send the string “Set Param $Param $Value” via serial connection.
2. Wait for the answer of the device with a timeout of 200 ms.
3. Check that the answer of the device is “OK”.
4. Send the string “Get Param $Param” via serial connection.
5. Wait for the answer of the device with a timeout of 200 ms.
6. Check that the answer is $Value.
Test parameters:
This test needs to be done for all writable parameters.
Parameter name	$Param	$Value
Refresh rate	refreshRate	5 [seconds]
Target temperature	targetTemp	77.5 [degree Celsius]
Cold temperature	coldTemp	-1.0 [degree Celsius]
WLAN SSID	SSID	My Home Network

### Write parameters via serial interface with invalid values

Requirement:	Verify that writing a parameter with an invalid value does not change	the parameter. The device should not crash.

Test setup:	Configure the device for simulated temperature input via serial	connection.	Send temperature data that puts the device out of pre-heat mode.	Check that the device is in measurement mode.

Test steps:	1. Send the string “Set Param $Param $Value” via serial connection.	2. Wait for the answer of the device with a timeout of 200 ms.	3. Check that the answer of the device is “ERROR”.	4. Send the string “Get Param $Param” via serial connection.	5. Wait for the answer of the device with a timeout of 200 ms.	6. Check that the answer is not $Value.

### Write parameters and check reaction of the output

Requirement:	Verify that written parameters are reloaded in the system by observing	a change in the output.
Test setup:	Configure the device for simulated temperature input via serial	connection.	Send temperature data that puts the device out of pre-heat mode.	Check that the device is in measurement mode.	Start sending simulated temperature data over serial connection.
Test steps:	1. Set the parameter ‘targetTemp’ to 60 °C over serial connection.	2. Wait until enough data points for time computation have been sent.	3. Get the parameter ‘timeDrink’ via serial connection as $Time_1.	4. Set the parameter ‘targetTemp’ to 40 °C over serial connection.	5. Get the parameter ‘timeDrink’ via serial connection as $Time_2.	6. Check that $Time_2 > $Time_1.

# Data processing
TBD

# Performance tests
### Test prediction accuracy with perfect data

Requirement:	Verify that the extrapolated temperatures are correct within a tolerance	of 5% when perfect test data is used. The time predictions shall be	checked in regular intervals.

Test setup:	Configure the device for simulated temperature input via serial	connection.
Check that the device is in pre-heat mode.
Start sending simulated temperature data over serial connection.

Test steps:	1. Check that the device is in measurement mode when the	temperature reaches 75 °C.	2. Get the parameter ‘timeDrink’ and compare it with the expected	value every 5 °C until 30 °C is reached. Check that the value has a	maximum deviation of 5%.

### Test prediction accuracy with data with artifacts in it
Requirement:	Verify that the predicted times do not deviate more than 20% when a	peak in the temperature data occurs.
### Test prediction accuracy with data with a changing slope

Requirement:	Verify that the predicted time adapts in a reasonable way when the	slope of the temperature curve is changing. Unrealistic results shall be	rejected until the prediction has stabilized.